ΨΗΦΙΑΚΟΣ ΕΛΕΓΧΟΣ

Β΄ ΕΞΑΜΗΝΟ 2016-7

(22Δ802)

Καθηγητής Πέτρος Π. Γρουμπός

( 2610 99 6449

Ώρες Γραφείου: Τετάρτη Πέμπτη Παρασκευή 11:00-12:00

Γραφείο: 1ος όροφος

Τομέας Συστημάτων & Αυτομάτου Ελέγχου

Τμήμα ΗΜ&ΤΥ

ΚΕΦΑΛΑΙΟ 2

Suppose that we are given a system, and we want to make it behave in some particular, specified way, in response to various inputs

This is the “Control Problem” – it can be thought of as choosing the input and changing the system so that it has a desired input-output behavior

For example, suppose that we want to make the output of the system

“track” (that is “match” or “follow”) a certain shape

We can think of this as making the system output, y, follow the system reference input, r. Let e be the error y = r-e

In the frequency domain, we can multiply inputs with transfer functions to get outputs

There are a great many techniques to do this controller design – this is the topic of various courses in control

• Feedback control systems

• Linear control system

• Digital control

• Adaptive control

• Intelligent Control

Some History of the Control-I

• Water clock (Greeks, 300 BC)

• Steam engine

• Classical Control (1930 – 1960)

– Feedback amplifiers, servomechanisms

– Continuous time, time invariant, SISO, mostly linear

– Root locus, Nyquist methods, Bode plot

Some History of the Control-II

• Modern Control – State space approach

– Kalman (1960)

– MIMO, time-varying

– Use of linear feedback to place all poles of LTI

systems

With the advent of low cost computation

digital control implementations became preferred

Digital Control Problem

• 	Usually trying to control a continuous time system, but using a digital controller to control it

• 	Need to be able to convert from continuous time signal to discrete time signal (“A/D converter”) – this is just sampling

• 	Need to be able to convert from discrete time to continuous time signal (“D/A converter”) – may ways to do this

Digital Signal Processing

• 	Continuous time signal source and continuous time result but use a digital representation to store process

• 	Need to be able to convert from continuous time signal to discrete time signal (“A/D converter”) – this is sampling and often compression

• 	Often need to be able to convert from discrete time to a continuous time signal (“D/A converter”) – many ways to do this

Quantization

Why Use Digital Control ?

• Often Cheaper

• Usually Smaller/lighter

• Usually needs Less power

• Often More precise

• Can Re-program

•	Can use same component (with different programming)  Generallity

Continuous Control (SISO case)

Digital Control (SISO case)

Two Approaches to Digital Control

System Design Specifications-I

• In time domain

– Stability

– Step response (rise time, settling time, overshoot, steady-state error)

• In frequency domain

– Filtering properties (high pass, low pass, band pass)

System Design Specifications-II

• Robustness

– Resistance to modeling errors, noise, small time variations

– Gain margin, phase margin, sensitivity

• Optimal Control

– Maximize or minimize a specified objective function

– Usually a cost on trajectory tracking error and on energy/control input; also may have costs based on trajectory endpoints

System Design Specifications-III

•	Usually the designer must extract this information from the customer

•	Translate the design needs into “intermediate specifications” – things like z plane or s plane pole locations

•	For digital control, selection of the sampling time T is an additional consideration (and perhaps associated filters for anti-aliasing)

Impact of this in emulation…

•	If you sample fast enough (>30 times system bandwidth)  not a big source of error

•	If sampling less than 30 times bandwidth, need to include the T/2 delay in the continuous time system model – so that the continuous time

controller is designed to compensate for it

Emulation Design vs Direct Digital

Control

• Emulation

– Can use continuous time methods (well developed)

– Few new tools needed

– Works well if sampling fast

– Mapping of control law from continuous time to discrete time is not exact

– Ignore continuous system response between sampling times

Emulation Design vs Direct Digital

Control

• Direct digital control

– Design of discrete time control law (and thus digital closed loop system) is exact for any sampling rate

– Ignore continuous system response between sampling times