## Slide 1: Body Parts on a Chip
Antonis Sakellarios

## Slide 2
BODY PARTS??

## Slide 3: The new “In” thing
C H I P S
  Everything available as chips, in chips or on chips…..!
  Fish n Chips…..! Now old stuff…! (Still tasty)
  Lab on a Chip over ten years old
  DNA chips (micro arrays) now routine..
  And now Organs on Chips….!
VARIETY OF CHIPS

## Slide 4
VARIETY OF CHIPS

## Slide 5: Physiology redefined
The zenith of applied physiology is:
  The ability to grow cells outside the body
    Cell & Tissue cultures
    Suffers from nutrient requirements, infections, etc.
  Develop a controlled sterile physiological micro-environment to maintain cells, tissues and organs
    Microfluidic chambers – 3D culture microenvironments
WHY CHIPS?

## Slide 6: Additional benefits of chips
Once fully successful, the new technology will do away with:
  Animal testing
    Drug development
    Toxicity assays
It will also allow in-depth understanding of the response of cells, tissues, organs and system to various environmental stimuli
WHY CHIPS?

## Slide 7
WHAT CHIP?

## Slide 8: What Is an Organ-on-a-Chip?
An Organ-on-a-Chip (OoC) is a microengineered system that mimics the structure and function of human organs using living cells cultured within microfluidic devices.
Size: A few centimeters long, transparent, polymer-based (often PDMS).
Core Components:
  Microfluidic channels
  Cell chambers (with organ-specific cells)
  Porous membranes
  Sensors or actuators

## Slide 9: When and why?

## Slide 10: How It Works?
Microfluidics simulate blood flow, air movement, or interstitial fluid.
Mechanical forces (like breathing motion or peristalsis) are recreated.
Multiple cell types (e.g., endothelial + epithelial) can be co-cultured.
Sensors allow real-time monitoring of pH, oxygen, metabolites, etc

## Slide 11: Applications
Application Area | Purpose
Drug development | Pharmacokinetics / Pharmacodynamics (PK/PD)
Toxicology | Organ-specific toxicity screening
Disease modeling | Inflammation, cancer, viral infections
Personalized medicine | Using patient-derived iPSCs or biopsies
Multi-organ models | Body-on-a-chip for systemic effects

## Slide 12: Examples of Organs-on-Chips
Lung-on-a-Chip: Simulates breathing; air and blood flow across a membrane.
Heart-on-a-Chip: Measures cardiomyocyte contractions and electrical signals.
Liver-on-a-Chip: For drug metabolism and hepatotoxicity.
Gut-on-a-Chip: Replicates microbiome, peristalsis, nutrient absorption.
Brain-on-a-Chip: Models blood-brain barrier and neuron-glia interactions.

## Slide 13: How to Build or Use One (Basic Steps)
Design the microfluidic layout (CAD-based).
Fabricate using soft lithography (PDMS casting).
Sterilize and seed organ-specific cells.
Connect perfusion system (pumps, reservoirs).
Monitor outputs (optical, electrical, biochemical).

## Slide 14
Experimental set-up for a generic two-organ system with supporting peripheral equipment

## Slide 15: Extended Process to Build an Organ-on-a-Chip
1. Define Biological Functionality
What organ do you want to mimic?
What physiological features must be recreated? (e.g., flow, stretch, barriers)
What cell types are needed?
2. Design Microfluidic Layout
Use CAD software (e.g., AutoCAD, SolidWorks) to:
  Design fluidic channels (blood, air, interstitial flow)
  Define chambers, valves, and interfaces (e.g., epithelial-endothelial separation)
  Incorporate sensing ports or electrodes if needed
I. Chip Design & Microfabrication

## Slide 16: Extended Process to Build an Organ-on-a-Chip
3. Fabricate the Master Mold
Use photolithography to create a mold on a silicon wafer:
  Spin-coat with photoresist (e.g., SU-8)
  Expose to UV light through a mask with the chip layout
  Develop and hard-bake to finalize the mold
4. Cast PDMS Chip
Mix PDMS base and curing agent (usually 10:1)
Pour over the mold and degas to remove bubbles
Cure in an oven (60–80°C for 1–2 hours)
Peel off and punch inlet/outlet holes
5. Bond to Substrate
Treat PDMS and glass/plastic substrate with oxygen plasma
Align and irreversibly bond to form closed channels
Sterilize via autoclaving, UV exposure, or ethanol wash
I. Chip Design & Microfabrication

## Slide 17
I. Materials for the chip

## Slide 18
I. Materials for the chip

## Slide 19: Extended Process to Build an Organ-on-a-Chip
6. Surface Treatment
Modify channels to promote cell adhesion:
  Coat with extracellular matrix proteins (e.g., collagen, fibronectin, Matrigel)
  Or use chemical modification (e.g., poly-L-lysine)
7. Cell Seeding
Introduce specific organ-relevant cells:
  Endothelial (blood vessels), epithelial (gut/lung), cardiomyocytes (heart)
Use appropriate media and conditions
Seed on different surfaces if co-culture is needed (e.g., two chambers separated by porous membrane)
II. Biological Functionalization

## Slide 20: Extended Process to Build an Organ-on-a-Chip
8. Maturation and Culture
Allow cells to grow to confluency and differentiate
Apply mechanical stimuli:
  Flow (via syringe or peristaltic pump)
  Stretch (for lung/heart chips)
  Electrical stimulation (for neurons/cardiomyocytes)
9. Introduce Dynamic Flow
Connect the device to a perfusion system:
  Use peristaltic/syringe pumps or pressure-driven systems
  Ensure shear stress mimics physiological conditions
Monitor parameters like:
  Flow rate
  Temperature
  pH and oxygen levels (optionally via sensors)
II. Biological Functionalization

## Slide 21: Extended Process to Build an Organ-on-a-Chip
10. Drug Testing / Disease Modeling
Introduce drugs, cytokines, toxins, or pathogens
Simulate disease states (e.g., hypoxia, inflammation)
11. Data Acquisition
Use real-time imaging (fluorescence, phase contrast)
Integrate with biosensors:
  TEER (barrier integrity)
  Electrochemical sensing
  Immunoassays or metabolite analysis
12. Data Interpretation
Measure response: viability, signaling, morphology, function
Compare to animal or 2D culture controls
Use computational models (in silico) for extrapolation
III. Experimentation & Analysis

## Slide 22: Extended Process to Build an Organ-on-a-Chip
10. Drug Testing / Disease Modeling
Introduce drugs, cytokines, toxins, or pathogens
Simulate disease states (e.g., hypoxia, inflammation)
11. Data Acquisition
Use real-time imaging (fluorescence, phase contrast)
Integrate with biosensors:
  TEER (barrier integrity)
  Electrochemical sensing
  Immunoassays or metabolite analysis
12. Data Interpretation
Measure response: viability, signaling, morphology, function
Compare to animal or 2D culture controls
Use computational models (in silico) for extrapolation
III. Experimentation & Analysis

## Slide 23
CHIP CONSTRUCT
& ASSEMBLY

## Slide 24
CHIP CONSTRUCT
& ASSEMBLY

## Slide 25
CHIP STRUCTURE

## Slide 26
CHIP STRUCTURE

## Slide 27
CHIP STRUCTURE

## Slide 28
Analysis of the OoC

## Slide 29
Analysis of the OoC

## Slide 30
Analysis of the OoC

## Slide 31
Current CHIPS
  Lung-on-a-Chip
  Heart-on-a-Chip
  Kidney-on-a-Chip
  Artery-on-a-Chip
  Gut-on-a-Chip
  Liver-on-a-Chip
  Brain
  Blood-brain barrier
Future CHIPS
  Bone marrow
  Skin
  Aerosol drug delivery
Human-on-a-Chip
SOME CHIPS

## Slide 32
LUNG ON A CHIP
Design:
Two parallel channels separated by a porous membrane
Air flows above the membrane (epithelial cells)
Blood substitute/media flows below (endothelial cells)
Side chambers apply cyclical stretch to simulate breathing

## Slide 33
LUNG ON A CHIP

## Slide 34: USES / APPLICATIONS
Advanced Physiology of the Alveolar-Endothelial interface & Respiration
Induced pulmonary injuries (pneumonitis)
  Microbes
  Toxins
Understanding of pulmonary inflammatory responses
Testing of aerosol drugs, nanoparticles, and environmental toxins
LUNG ON A CHIP
Benefits:
Realistic gas exchange environment
Demonstrated better prediction of inflammatory response than animal models

## Slide 35
HEART ON A CHIP
Design:
Microchambers or cantilevers seeded with cardiomyocytes
Can apply electrical stimulation and/or mechanical stretch
Flexible substrates allow observation of contractile force

## Slide 36
HEART ON A CHIP

## Slide 37: USES / APPLICATIONS
Advanced physiology of myocardial contractility
Monitoring of myocyte loads and stresses
Induced myocyte injuries
  Ischemic
  Toxic
Physiological & pathological responses of myocytes
Development of personalized cardiac therapies
Disease modeling: Long QT syndrome, cardiomyopathies
HEART ON A CHIP
Benefits:
Measures real-time beating behavior, force, and conduction velocity
Enables dose-response curves on cardiac cells

## Slide 38
HEART ON A CHIP

## Slide 39
KIDNEY ON A CHIP
NEPHRON

## Slide 40
KIDNEY ON A CHIP

## Slide 41: USES / APPLICATIONS
💊 Drug Testing
Detecting nephrotoxicity from drugs like cisplatin, gentamicin, tenofovir
Evaluating early-stage kidney injury with biomarker readouts
🧬 Disease Modeling
Diabetic nephropathy
Polycystic kidney disease (PKD)
Ischemia-reperfusion injury
🔬 Physiological Studies
Understanding solute and water transport
Investigating the effect of flow, pressure, and pH on renal function
Reproducing glomerular filtration rate (GFR)–like behavior
KIDNEY ON A CHIP
Benefits
Human cell-based
Dynamic flow and shear stress
Real-time functional monitoring
Scalable and modular

## Slide 42
GUT ON A CHIP

## Slide 43
GUT ON A CHIP

## Slide 44
GUT ON A CHIP

## Slide 45: USES / APPLICATIONS
Advanced Physiology & Biochemistry
Motility disorders
Infectious gut diseases
Food allergies
GI models of neoplastic diseases
Drug testing
GUT ON A CHIP
Benefits:
Can maintain commensal bacteria long-term
Captures host-microbiome-immune interactions

## Slide 46
LIVER ON A CHIP
Microfluidic Design
Mimics liver sinusoid architecture
Features dynamic flow that replicates blood perfusion
Allows zonal oxygen gradients, which are important for replicating liver lobule function (zone 1 to zone 3 behavior)

## Slide 47
LIVER ON A CHIP

## Slide 48: USES / APPLICATIONS
Advanced Biochemistry & Physiology
Drug Reactions / Toxicity
Infectious diseases
Tumors (Primary / secondary)
LIVER ON A CHIP

## Slide 49
Brain-on-a-Chip / Blood-Brain Barrier-on-a-Chip

## Slide 50
🔧 Design:
Co-culture of neurons, astrocytes, and endothelial cells
3D matrix or layered chip mimicking BBB
Microfluidic flow simulates nutrient exchange
🩺 Application:
Study of BBB permeability, neurotoxicity, Alzheimer’s
Screening of CNS drugs
Modeling inflammatory diseases (e.g., multiple sclerosis)
Brain-on-a-Chip / Blood-Brain Barrier-on-a-Chip
📊 Benefits:
Improved modeling of tight junction integrity
Reduces false negatives in CNS drug screening

## Slide 51
MULTIPLE TISSUES ON A CHIP

## Slide 52: USES / APPLICATIONS
MULTIPLE TISSUES ON A CHIP
Modular constructs of any tissues selected
Cellular & Tissue interactions and responses in health and disease conditions
Experimental research / Interventions
Models of disease involving multiple tissues / organs

## Slide 53
ARTERY ON A CHIP
ORGAN ON A CHIP

## Slide 54: USES / APPLICATIONS
Normal and diseased arteries can be loaded on the chip
Perfusion and Superfusion fluids can be customized
Endothelial / Muscular responses to a wide variety of stimuli (physical & chemical) can be studied
ARTERY ON A CHIP

## Slide 55
SPLEEN ON A CHIP
ORGAN ON A CHIP

## Slide 56: USES / APPLICATIONS
Immunology
Hematology
Drug Testing
Infectious diseases
SPLEEN ON A CHIP

## Slide 57: 3D cell models for organ-on-a-chip applications

## Slide 58: 3D cell models for organ-on-a-chip applications

## Slide 59
HUMAN BODY ON A CHIP

## Slide 60
HUMAN BODY ON A CHIP

## Slide 61: USES / APPLICATIONS
Customized constructs based on multiple organs and systems
Will allow detailed study of systemic physiology & pathology
Development of experimental disease models on a whole-body aspect
HUMAN BODY ON A CHIP

## Slide 62: Integration with In Silico Modeling
Coupled with computational models (FEM, CFD, AI) to:
Simulate transport phenomena
Optimize chip design
Predict drug response or toxicity
Personalize based on patient parameters

## Slide 63: Integration with In Silico Modeling

## Slide 64: 1. Design and Engineering Optimization
✅ What It Does:
Simulates fluid dynamics, shear stress, and pressure gradients (using CFD)
Optimizes chip geometry and channel layout for realistic conditions
Models transport of nutrients, drugs, gases, and waste
🔧 Tools Used:
Computational Fluid Dynamics (CFD) – e.g., ANSYS Fluent, COMSOL
Finite Element Method (FEM) – for mechanical strain/stress modeling
Agent-based models – simulate cell behavior and interactions
In silico modelling

## Slide 65: 2. Physiological and Cellular Simulation
✅ What It Does:
Models cell signaling, metabolism, and electrophysiology under chip conditions
Predicts organ-specific responses (e.g., contraction in heart, GFR in kidney)
Simulates multi-scale interactions: molecular → cellular → tissue
💡 Example:
Use of ODE/PDE models to represent how liver cells metabolize a drug inside a liver-on-a-chip
In silico modelling

## Slide 66: 3. Drug Response Prediction
✅ What It Does:
Simulates pharmacokinetics/pharmacodynamics (PK/PD) within the chip
Predicts toxicity thresholds and dose-response curves
Enables virtual screening of drug candidates before live chip testing
🎯 Benefit:
Reduces the number of wet-lab trials needed
Supports regulatory approval with quantitative predictions
In silico modelling

## Slide 67: 4. Multi-Organ and Systemic Simulation
✅ What It Does:
Connects different OoC modules virtually (e.g., gut–liver–kidney)
Simulates inter-organ communication, like hormone signaling or drug metabolism
Reproduces whole-body pharmacology (Body-on-a-Chip + computational body model)
In silico modelling

## Slide 68: 5. Data Integration and Machine Learning
✅ What It Does:
Analyzes real-time chip data (biosensors, imaging) for predictive modeling
Applies AI/ML models to identify biomarkers or predict outcomes
Builds digital twins of chips or even patients
In silico modelling

## Slide 69: 🎯 Why It Matters
Purpose | Impact
Design optimization | Better chip performance
Reduced trial-and-error | Saves time and resources
Personalized predictions | Enables precision medicine
Mechanistic understanding | Reveals hidden biological insights
Regulatory confidence | Supports reproducibility and safety
In silico modelling

## Slide 70: Ethical and Regulatory Considerations
May reduce animal testing → aligns with 3Rs (Replace, Reduce, Refine).
Regulatory approval requires standardization and validation.
Challenges:
  Complexity of models
  Manufacturing scale-up
  Acceptance in clinical pipelines