## Slide 1
“Introduction to Monte Carlo Simulations and Evolution of Anthropomorphic Phantoms”
Panagiotis Papadimitroulas
panpap@bioemtech.com
PhD Medical Physics
Project Director @ BIOEMTECH
Patras, 2022
Notes: 1
BET Solutions

## Slide 2
Overview
Radiation Physics & Monte Carlo simulations
GATE simulation toolkit
Evolution of Computational Phantoms
Anthropomorphic Phantoms
Examples / Applications

## Slide 3
Overview
Radiation Physics & Monte Carlo simulations
GATE simulation toolkit
Evolution of Computational Phantoms
Anthropomorphic Phantoms
Examples / Applications

## Slide 4
Nuclear Imaging: SPECT & PET
In both cases we image the concentration of a biomolecule non – invasively
Need to optimize and personalize the diagnoistic imaging protocols!
SPECT imaging
PET imaging

## Slide 5
CT Imaging
CT scans  X-ray beam irradiating the patient
Complete rotation of the source around the patient.

## Slide 6
Dosimetry
Since the advent of X-rays in 1895 (by Wilhelm Conrad Roentgen), it has been known that exposure to ionizing radiation can be harmful to humans.
Current research is challenging the paradigm that the quantity “absorbed dose” is the best to use in predicting biological effects. Correlation to individualized patient characteristics.
Absorbed dose is the main quantity of interest:
MIRD – ICRP – RADAR: main systems to estimate absorbed dose

## Slide 7
Radiotherapy - Dosimetry
External or Internal radiation  Deposited Energy
Knowledge of the distribution and the amount of Absorbed Dose.
Preclinical Dosimetry
Brachytherapy
Particle Therapy - proton

## Slide 8
Monte Carlo Introduction
Source: www.scopus.com
“Monte Carlo method is a statistical approach to solve deterministic problems and define a specified system using random number generators”
MC techniques took their name form the Monte Carlo Casino.
>40 years MC techniques are applied in Medical Physics.

## Slide 9
Monte Carlo Examples
1D example: Coin Toss
Same probability to get the “head” or the “tail”.
Expected ratio value between “head” or “tail” is 1.
The more coin tosses the more our statistics is converging to the expected value. (Random draws to estimate the value)
Nb of coin tosses
Nb of heads / nb of tails

## Slide 10
Monte Carlo Examples
2D example: Calculation of π
Random processes are repeated many times so that result becomes statically realistic
Draw a square on the ground & inscribe a quadrant.
Uniformly scatter some objects of uniform size.
Count the number of objects inside the circle and the total number of objects.
The ratio of the two is an estimation of the ratio of the two areas, which is p/4.

## Slide 11
Monte Carlo Examples
3D example: Nuclear Imaging
Random processes are repeated many times
so that result becomes statically realistic
Looking for the expected value!
108
106
107

## Slide 12
Monte Carlo Navigation
Random sample must follow
the laws of physics
γ
Which distance?
Which effect?
Which deflection angle?
Which distance?
Which effect?
Which distance?
Which energy lost?
Which deflection angle?

## Slide 13
Monte Carlo Geometries
Building a world in Monte Carlo simulation
A world is a virtual volume that contains all system geometries

## Slide 14
Overview
Radiation Physics & Monte Carlo simulations
GATE simulation toolkit
Evolution of Computational Phantoms
Anthropomorphic Phantoms
Examples / Applications

## Slide 15
GATE MC toolkit
Geant4 Application for Emission Tomography, Transmission Tomography and Radiotherapy
History
Open-source software dedicated to the simulation of imaging (SPECT, PET, CT, optical and RT)
Based on the Geant4 toolbox
First release of GATE in May 2004
26 releases since that date (last release GATE v9.1)

## Slide 16
GATE MC toolkit
GATE: Geant4 Application for Emission Tomography, Transmission Tomography and Radiotherapy
Technical Features
GATE is based on Geant4 (written in C++)
GATE is user-friendly without any C++ writing (using macros)
GATE is flexible enough to model almost any detector design
GATE can handle analytical or voxelized phantoms
GATE can run on a cluster architecture and on grid

## Slide 17
GATE MC toolkit
GATE: Geant4 Application for Emission Tomography, Transmission Tomography and Radiotherapy
Broad range of applications
Detector Design
Optimization of acquisition and processing protocols
Assessment of quantification methods
Estimation of the system matrix used in tomographic reconstruction
Use of voxelized anthropomorphic models (CT – MR images)
Dosimetry

## Slide 18
OpenGATE collaboration
16 labs, sharing developments and validation studies regarding GATE, working together to make these developments publicly available
OpenGATE collaborators meet twice a year, and communicate any time via a gate-devel mailing list
The OpenGATE collaboration steering committee consists of one representative of each of the 16 labs
The role of the collaboration is:
Upgrade GATE to follow the Geant4 releases
Add new functionalities to GATE
Organize training schools
http://www.opengatecollaboration.org/

## Slide 19
GATE landmarks
“GATE: A simulation toolkit for PET and SPECT” S. Jan et al., Phys. Med. Biol. 49, 4543–4561 (2004)
“GATE V6: A major enhancement of the GATE simulation platform enabling modelling of CT and radiotherapy” S. Jan et al., Phys. Med. Biol. 56, 881-901 (2011)
“A review of the use and potential of the GATE Monte Carlo simulation code for radiation therapy and dosimetry applications” D. Sarrut et al., Med. Phys. 41(6), 064301 (2014)
“Advanced Monte Carlo simulations of emission tomography imaging systems with GATE”
D. Sarrut et al., Phys. Med. Biol. 14; 66(10) (2021)

## Slide 20
GATE Core

## Slide 21
GATE: Basic steps in NM
Geometry Description
Definition of Physical Processes
Particle Generation Source Definition
Data Processing

## Slide 22
GATE: Applications in NM
Scatter + other Corrections
Scanner Design
Optimization
Data Analysis
Image Reconstruction
Algorithm Testing
Monte Carlo Simulations

## Slide 23
GATE: What Can We Do?
Simulate realistic exams (MC in clinical practice)
Use MC to optimize:
Acquisition protocol (injected dose, acquisition time, dedicated for each patient)
Algorithms for data corrections and reconstruction
Quantitative analysis
Dosimetry studies
We need something more than simple phantoms !!!
Metabolic imaging
Receptor imaging
Oncology

## Slide 24
Overview
Radiation Physics & Monte Carlo simulations
GATE simulation toolkit
Evolution of Computational Phantoms
Anthropomorphic Phantoms
Examples / Applications

## Slide 25
Evolution… Stylized Phantoms 1960s-2000s
1st attempt at developing a computational anthropomorphic phantom were reported by Fisher and Snyder at ORNL (1960s).
  Adult phantom: shapes (elliptical cylinder, cones, spheres etc)
  Children phantoms: scaled-down versions of the adult
  Pregnant
Since 1960s over than 130 phantoms have been reported
Large list of stylized phantoms were continuously extended

## Slide 26
Evolution… Stylized Phantoms 1960s-2000s
1st heterogeneous phantom: 1969 by Snyder (MIRD-5 Phantom)
The MIRD-5 phantom was composed of:
skeleton, lungs and remainder soft tissue
Representation of the ICRP Reference-man:
Healthy adult Caucasian male 20-30 y old, 70 kg
1978: Improvement of the phantom with >20 organs

## Slide 27
Evolution… Voxel Phantoms 1980s-2000s
Development of anatomically realistic models:
Powerful computers
Tomographic imaging technologies
Ability of visualization the internal structures in 3D
Storing in digital formats
Till 2010, a list of 74 anthropomorphic phantoms was reported*
There is always the NEED for a REFERENCE MODEL.
*Handbook of Anatomical Models for Radiation Dosimetry

## Slide 28
Creation… of a Voxel Phantom
4 Basic Steps
1) Acquire a set of tomographic images (e.g. CT, MR) that cover the entire volume of body
2) Identify organs or tissues of interest (e.g. lungs, liver, skin, bones) from the original image slice assigning every pixel with an identification number
3) Specify the density and chemical composition of the tissues
4) Register the segmented image slices into a 3D volume that can be used for 3D visualization and imported in MC simulator.

## Slide 29
Evolution… BREP Phantoms from 2000s to present
BREP – Boundary Representation phantoms
Prof. P. Segar’s PhD thesis was the first publication that systematically described the NURBS-based modeling techniques.
Over 30 BREP phantoms have been reported till now...
The NURBS is widely used in 3D computer graphics to describe three-dimensional surfaces. A NURBS surface is a bidirectional parametric representation of an object.
Points on a NURBS surface are defined by two parametric variables, u and v, usually representing longitude and latitude respectively. Points defined in Cartesian coordinates (x, y, z) can easily be converted into surface coordinates (u and v) and vice versa.

## Slide 30
NURBS… Realistic Phantoms
Model of the human body computed
Accurate with respect to the internal structure of the human body
Phantoms of children, teenagers and adult, male and female, pregnant and animals for preclinical applications exist
3D and 4D model
4-D BREP Phantom
VIP-Man phantom
Mice Ncat phantom
Phantom that can be voxelized using different resolution
Perform phantom based study
Ground truth know (anatomy – motion)

## Slide 31
MESH… Triangular based Phantoms
Triangular based mesh geometry
Based on triangles or quadrilaterals
Simple to store (3D points)
Allow complex shape
CAD modeling (artificial implants, scanner elements, etc.)
Anatomical details derived from other imaging modalities such as example MRI (arteries, spinal cord, atheroma, etc.)
Accuracy is depending to the number of triangles used to describe the geometry (time consuming)

## Slide 32
Overview
Radiation Physics & Monte Carlo simulations
GATE simulation toolkit
Evolution of Computational Phantoms
Anthropomorphic Phantoms
Examples / Applications

## Slide 33
Anthropomoprhic Phantoms… MIRD-5 ORNL
ORNL – Oak Ridge National Laboratory by Fisher and Snyder (1966)
Adult phantom
Dosimetry calculations
Many years of developments
Anterior view of the principal organs in the head and trunk of the adult phantom developed by Snyder et al

## Slide 34
Anthropomoprhic Phantoms… ADELAIDE
The ADELAIDE work was one of the first attempts for pediatric voxel based phantoms.
2 voxel phantoms in 1990s - 8 week old baby & 7 year old child
Purpose: Torso organ doses from CT
In 1996, use of DICOM.
A GE CT scanner produces 512x512x54 images (10mm interval)
Manual segmentation
30 separate organs identified

## Slide 35
Anthropomoprhic Phantoms… MCATNCATXCAT
The 4D Mathematical Cardiac Torso (MCAT) – 20 years ago
Developed for NM (SPECT/PET)
based on MIRD model.

## Slide 36
Anthropomoprhic Phantoms… MCATNCATXCAT
The 4D NURBS Cardiac Torso (NCAT) – based on NURBS
More realistic anatomy modeling Cardiac and respiratory motion

## Slide 37
Anthropomoprhic Phantoms… MCATNCATXCAT
The 4D Extended Cardiac Torso (XCAT) – based on NURBS & SD*
Enhance the ability to represent human anatomy and physiology.
Based on the high resolution Visible Male and Female anatomical datasets from the NLM.
XCAT includes more that 9000 anatomical objects over the entire human body
*SD: Subdivision surfaces to model structures with an arbitrary topological type.

## Slide 38
Personalization on Phantoms
The development of more and more computational anthropomorphic phantoms is still rising.
Interested in accuracy and personalization:
Pediatric (newborn, infants, teenagers)
Pregnant
Different body types (Caucasian, Japanese, Korean, Chinese)
Postures

## Slide 39
Deforming Phantoms… Creating Population
*MC-LDDMM: multichannel large deformation diffeomorphic metric mapping

## Slide 40
Overview
Radiation Physics & Monte Carlo simulations
GATE simulation toolkit
Evolution of Computational Phantoms
Anthropomorphic Phantoms
Examples / Applications

## Slide 41
Example… Objectives
Goal
Creation of a realistic simulations for PET and SPECT incorporating:
High statistics
Accurate physical processes
Patient anatomical and functional variability

## Slide 42
Methodology Steps
Imaging system modeling The imaging system (SPECT or PET) is described in GATE and the simulation is validated by comparing experimental and simulation data
Attenuation map Anthropomorphic models are used for describing whole-body and brain (head) patient’s anatomy respectively. Each organ is defined by it’s corresponding tissue
Activity map The activity distributions inserted in GATE are extracted from clinical data, according to radiotracer’s concentration of each organ
Tumors extraction – Segmentation Tumors can be inserted in the models according to the CT data (e.g. delineating them from clinical images, resulting to segmentation masks)
Execution Need of high computational resources for realistic simulations (Grids, GPU, clusters)

## Slide 43
Simulation preparation: Assignment of Activity
Clinical PET system
Simulated system in GATE
Step 1:
Describe the system in GATE
Step 2:
Validate simulation
Chart: Spatial Resolution
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Simulation | 1.8389 | 1.935 | 2.2266 | 2.5573 | 2.8919 | 3.1716 | 3.5967 | 3.7345 | 4.227 | 4.3474 | 4.5577
Experimental | 2.0586 | 2.0943 | 2.3129 | 2.6157 | 2.9629 | 3.0857 | 3.3857 | 4.1786 | 4.8286

## Slide 44
Simulation preparation: Assignment of Activity
Clinical
PET image
Adapted
XCAT phantom
Case 1:
Obtain radioactivity from clinical images
Case 2:
Use bio-distribution data

## Slide 45
Simulation preparation: Assignment of Activity
Tumor extraction and creation of the 3D tumor mask
Application of correction techniques e.g. PVC in PET

## Slide 46
Example PET: Heterogeneous Oncology
  Correction of the PVE, which is responsible for the limited resolution in the borders of heterogeneous areas
  PVC activity maps improved the resulted images compared to the clinical data

## Slide 47
Example SPECT: Scans using XCAT
99mTc-MDP bio-distribution
Real Simulated
Planar MDP
Anterior scan
Real Simulated
Planar MDP
Posterior scan
99mTc-SestaMIBI biodistribution
XCAT phantom
Simulated cardiac SPECT

## Slide 48
Example Molecular & preclinical imaging
GATE simulation
4D MOBY phantom
Simulation
result

## Slide 49
Applications (I)
  Provide the ground truth to validate and evaluate different acquisition protocols, processing tools and reconstruction algorithms
  Optimization of medical imaging protocols to reduce the absorbed dose in patients and incorporate their personalized characteristics
Real distribution
No Att. Cor.
With Att. Cor.
All photons
20% energy window
Exclude scatter
Α
Β
Γ
Δ
Ε
ΣΤ
Ζ
Η
Θ

## Slide 50
Applications (II)
  Optimize imaging protocols to achieve best imaging performance
  Optimization of medical imaging protocols to reduce the absorbed dose in patients and incorporate their personalized characteristics

## Slide 51
Applications (III)
  Dosimetry calculation of the presented simulations.
  Incorporation of patient motion in simulations
  Use of other anthropomorphic phantoms
  Extension towards small animal imaging data

## Slide 52
Applications S-values (IV)
S-value Definition:
“The S-value is defined as the product of the emitted energy per disintegration and the absorbed fraction for the given combination of source and target regions, for the type of radiation emitted, divided by the mass of the target region ”*
in Gy/(Bq×Sec)

## Slide 53
Applications S-values (IV)
We calculated the S-values (SADRs) for several radiopharmaceuticals using heterogeneous sources for preclinical and pediatric applications.
Provide accurate dosimetric schemes, taking into account the activity distribution within the body and the whole spectrum of the injected radioisotope.
The procedure is validated with previously published data in preclinical studies.

## Slide 54
Applications S-values (IV)
Validation of the procedure using GATE platform was applied comparing previously reported data with Geant4 to our simulated data with GATE and XCAT phantom
Liver  Kidneys & Liver  Liver for monoenergetic photons
Differences: 0-5 %

## Slide 55
Applications S-values (IV)
Simulation Preparation - Obtain Radioisotope Biodistribution
S-values in 3-4 time stamps to obtain the S-value modification due the TAC per organ of interest.

## Slide 56
Applications S-values (IV)
S-values for 6 phantoms, grouped by organ

## Slide 57
Applications Preclinical Imaging (V)
Simulation of the energy spectrum
Preparation of the MOBY mouse model
Simulation of the CMOS detector (CsI crystal: ~12x12 cm2)
Simulation of mouse X-ray irradiation
Simulated X-ray image

## Slide 58
Applications Preclinical Imaging (V)
No NPs
10mgAu in liver
0.4% PW
20mgAu in liver
0.8% PW
40mgAu in liver
1.64% PW
5mgAu in liver
0.2% PW
Chart: PW Au concentration (%)
| 0 | 0.2 | 0.4 | 0.8 | 1.64
Liver Accumulation | 2.583 | 4.052 | 4.812 | 5.904 | 7.508
Simulation of different concentrations of GNPs in liver

## Slide 59
Applications Preclinical Imaging (V)
Merged slices of simulated dose maps in a mouse model with different concentrations of GNPs in liver
40 mg Au – 0.4% per weight,
10 mg Au – 1.64% per weight
no GNPs present

## Slide 60
Applications Preclinical Imaging (V)
No GNPs 2.5mg 5mg 10mg 15mg 25mg 30mg
X-rays using different concentrations in leg muscle.
ROI of measurements

## Slide 61
Applications Creation of a Sheep Model (VI)
Mouse / Rat Sheep Human / Anthropomorphic
Already available (MOBY)
Need to be modeled using a clinical CT
Already available (XCAT)

## Slide 62
Applications Creation of a Sheep Model (VI)
Sheep
CT acquisition
Obtain CT data
Use segmentation algorithms and 3D-slicer
(Veterinary)
Creation of a novel
sheep model

## Slide 63
Radiobiology using Geant4-DNA
Biological & Physical simulations
G4DNA project www.geant4-dna.org
Radiobiology
Microdosimetry
Radiochemistry
Biological damage
DNA model
Cell & nucleus dosimetry

## Slide 64: Ευχαριστώ πολύ Απορίες … Συζήτηση …

## Slide 65
“Introduction to Monte Carlo Simulations and Evolution of Anthropomorphic Phantoms”
Panagiotis Papadimitroulas
panpap@bioemtech.com
PhD Medical Physics
Project Director @ BIOEMTECH
Patras, 2022
Notes: 65
BET Solutions