## Slide 1
Ατμοσφαιρική Ρύπανση (ΕΕΕ423)
Μάθημα 6ο
Αριθμητικά μοντέλα ατμοσφαιρικής ρύπανσης
23/11/2017
Ελένη Αθανασοπούλου
1

## Slide 2
Δομή Μαθήματος
Εισαγωγή
Χωρικές και χρονικές κλίμακες εφαρμογής μοντέλου ρύπανσης/ποιότητας ατμόσφαιρας
Κατηγοριοποίηση αριθμητικών μοντέλων
Χωρική και χρονική διακριτική ικανότητα εφαρμογής
Δεδομένα εισόδου σε μια αριθμητική προσομοίωση
Συνδυασμός με πειραματικά δεδομένα
Εφαρμογές μοντέλου – Έλεγχοι ευαισθησίας

## Slide 3
Εισαγωγή
Πηγή: ΕΔΕΤ. Οι “Υπερυπολογιστές” αξιοποιούνται σε επιστημονικές εφαρμογές που απαιτούν την εκτέλεση πολλών εκατομμυρίων μαθηματικών πράξεων ή/κα ιτην επεξεργασία μεγάλου όγκου δεδομένων.
Ορισμός: Αριθμητικό μοντέλο είναι η μαθηματική περιγραφή μιας διαδικασίας. Ένα ατμοσφαιρικό υπολογιστικό μοντέλο είναι η κωδικοποίηση σε υπολογιστή της αναπαράστασης/προσομοίωσης των δυναμικών, φυσικών, χημικών και ακτινοβολιακών διεργασιών στην ατμόσφαιρα.
Notes: Οι “Υπερυπολογιστές” είναι υπολογιστικά συστήματα που αξιοποιούνται σε επιστημονικές εφαρμογές οι οποίες απαιτούν την εκτέλεση πολλών εκατομμυρίων μαθηματικών πράξεων ή την επεξεργασία μεγάλου όγκου δεδομένων. Λόγω αυτών των απαιτήσεων τέτοιου είδους προβλήματα είτε θα χρειάζονταν απαγορευτικά μεγάλο χρόνο για να ολοκληρωθούν σε έναν απλό υπολογιστή γραφείου είτε λόγω περιορισμένων πόρων (π.χ. κεντρική μνήμη, αποθηκευτικός χώρος) δεν είναι εφικτό να πραγματοποιηθούν καθόλου. Οι υπερυπολογιστές ξεπερνούν τους περιορισμούς αυτούς χρησιμοποιώντας εξειδικευμένο υλικό τελευταίας τεχνολογίας κάθε χρονική στιγμή, εκμεταλλευόμενοι παράλληλα την υπολογιστική ισχύ από πολλαπλές υπολογιστικές μονάδες. Ένας υπερυπολογιστής σήμερα είναι στην πραγματικότητα ένα σύστημα από εκατοντάδες ή και χιλιάδες υπολογιστές (στους οποίους αναφερόμαστε συνήθως ως “κόμβους) που επικοινωνούν μεταξύ τους χρησιμοποιώντας ένα πολύ γρήγορο δίκτυο και οι οποίοι συνεργατικά μπορούν να επιλύουν προβλήματα με μεγάλη ταχύτητα.
https://www3.epa.gov/scram001/aqmindex.htm
https://www5.in.tum.de/forschung/simlab/course2010_files/course_mat/Frisch_Intro_NumericalModelling.pdf
https://pcmdi.llnl.gov/about.html , https://www3.epa.gov/scram001/aqmindex.htm , https://www.aeroqual.com/air-pollution-modelling , https://en.wikipedia.org/wiki/List_of_atmospheric_dispersion_models
In atmospheric models, time-dependent processes
are mathematically described by ordinary differential equations. Space- and
time-dependent processes are described by partial differential equations. Ordinary
and partial differential equations are replaced with finite-difference or other
approximations, then computerized and solved.Computer models also solve parameterized and empirical equations. A parameterized
equation is an equation in which one parameter is expressed in terms of
at least two other parameters. The equation of state, which relates pressure to
temperature and air density, is a parameterized equation. An empirical equation
is an equation in which one parameter is expressed as an empirical function (e.g.,
a polynomial fit) of at least one other parameter. Whereas parameterized equations
are derived from insight, empirical equations do not always make physical
sense. Instead, they reproduce observed results under a variety of conditions. In this
text, computer modeling of the atmosphere is discussed. Such modeling requires
solutions to ordinary differential equations, partial differential equations, parameterized
equations, and empirical equations.
Since the advent of atmospheric computer modeling in 1948, models have been
applied to study weather, climate, and air pollution on urban, regional, and global
scales.
Historically, meteorological models have been used to simulate weather, climate,
and climate change. Photochemical models have been used to study urban, regional,
and global air-pollution emission, chemistry, aerosol processes, and transport of pollutants. Only recently have meteorological models merged with photochemical
models to tackle these problems together.
One purpose of developing a model is to understand better the physical, chemical,
dynamical, and radiative properties of air pollution and meteorology. A second
purpose is to improve the model so that it may be used for forecasting. A third
purpose is to develop a tool that can be used for policy making. With an accurate
model, policy makers can try to mitigate pollution problems.
… In sum, weather, climate, and air pollution can be modeled by taking into account
a fairly reasonably well-defined set of physical, chemical, and/or dynamical equations.

## Slide 4
Εισαγωγή
Notes: https://pcmdi.llnl.gov/about.html
https://www3.epa.gov/scram001/aqmindex.htm
https://www.aeroqual.com/air-pollution-modelling
https://en.wikipedia.org/wiki/List_of_atmospheric_dispersion_models

## Slide 5
Εισαγωγή
Γιατί χρειαζόμαστε τις αριθμητικές προσομοιώσεις?
Γιατί συγκεκριμένες μελέτες δεν αντιμετωπίζονται με πειράματα , πχ πρόγνωση καιρού ή/και ρύπανσης είτε επιχειρησιακή, είτε έκτακτη (ατύχημα)
Volcano episode: 14.04. – 18.04.2006
Spatial distribution of hourly concentrations
(m-3) of ash particles
Notes: Firstly, you can assess a completely hypothetical situation before it occurs. For example, an industrial operation may propose a new facility. In their design they might specify a stack of several meters tall, emitting pollutants from a known process. Using a model the emissions can be roughly quantified.
These emissions can be fed into a model, which can predict the emissions spatially around the source. This analysis might show that concentrations are too high based on a given operating mode, or might show that under certain wind conditions the concentrations in a residential area are unacceptably high.
The power of this is that the problem can be solved before it even exists. Often, industrial emitters need to demonstrate their environmental impact. The severity of their impact dictates whether their emissions are allowed, or need further permitting.
Similarly, a model can be used to predict alternative situations. For instance, the facility may decide that it wants to upgrade its infrastructure, changing fuel or installing better, more effective scrubbers. The emissions given these changes can then be quantified. These are called scenarios.

## Slide 6
Εισαγωγή
Γιατί χρειαζόμαστε τις αριθμητικές προσομοιώσεις?
Γιατί συγκεκριμένες μελέτες δεν αντιμετωπίζονται με πειράματα , πχ πρόγνωση καιρού ή/και ρύπανσης είτε επιχειρησιακή, είτε έκτακτη (ατύχημα)
Είναι δύσκολες οι συνθήκες για να στηθεί και να εκτελεστεί πείραμα (π.χ. σε περιοχές με ακραία καιρικά φαινόμενα/χιονοκάλυψη)

## Slide 7
Εισαγωγή
Γιατί χρειαζόμαστε τις αριθμητικές προσομοιώσεις?
Το στήσιμο πειραμάτων είναι κάποιες φορές δύσκολο, χρονοβόρο και κοστοβόρο

## Slide 8
Εισαγωγή
Γιατί χρειαζόμαστε τις αριθμητικές προσομοιώσεις?
Η χωρική κάλυψη των αποτελεσμάτων των μοντέλων σε σχέση με τις σημειακές μετρήσεις ρύπανσης
Αριθμητικά μοντέλα
Πειραματικές μετρήσεις
 Άμεση απόκριση στις
πραγματικές εκπομπές,
μετεωρολογικές συνθήκες
 Περιορισμένη
χωρική - χημική πληροφορία
 Αναλυτική
χωρική - χημική πληροφορία
 Τυπικές εκπομπές,
Mετεωρολογικά δεδομένα
μοντέλου

## Slide 9
Εισαγωγή
Γιατί χρειαζόμαστε τις αριθμητικές προσομοιώσεις?
Εκτέλεση ελέγχων ευαισθησίας για π.χ.
Έλεγχος ρύπανσης μέσω προσδιορισμού του ποσοστού επίδρασης συγκεκριμένων πηγών στις συγκεντρώσεις ρύπανσης

## Slide 10
Εισαγωγή
Γιατί χρειαζόμαστε τις αριθμητικές προσομοιώσεις?
Εκτέλεση ελέγχων ευαισθησίας για π.χ.
Έλεγχος ρύπανσης κατά την εγκατάσταση μιας νέας πηγής: θα επιβαρύνει την ατμόσφαιρα σε μη ανεκτά για τον άνθρωπο επίπεδα?
Έλεγχος μετριασμού ρύπανσης σε υποθετικά σενάρια μεταβολής των χαρ/κων πηγής
Model run showing surface NO2 from point sources in Korea. Credit: NCAR/Louisa Emmons

## Slide 11
Εισαγωγή
Γιατί χρειαζόμαστε τις αριθμητικές προσομοιώσεις?
Εκτέλεση ελέγχων ευαισθησίας για π.χ.
Έλεγχος μεταβολής ρύπανσης σε μελλοντικά κλιματικά σενάρια

## Slide 12
Εισαγωγή
Γιατί χρειαζόμαστε τις αριθμητικές προσομοιώσεις?
Εκτέλεση ελέγχων ευαισθησίας για π.χ.
Πρόβλεψη αέριας ρύπανσης κατά την εφαρμογή νέου προγράμματος μετριασμού ρύπανσης, με σκοπό τον έλεγχο αποτελεσματικότητας του προγράμματος στην μείωση των επικίνδυνων για την υγεία ρύπων.

## Slide 13
Δομή Μαθήματος
Εισαγωγή
Χωρικές και χρονικές κλίμακες εφαρμογής μοντέλου ρύπανσης/ποιότητας ατμόσφαιρας
Κατηγοριοποίηση αριθμητικών μοντέλων
Χωρική και χρονική διακριτική ικανότητα εφαρμογής
Δεδομένα εισόδου σε μια αριθμητική προσομοίωση
Συνδυασμός με πειραματικά δεδομένα
Εφαρμογές μοντέλου – Έλεγχοι ευαισθησίας

## Slide 14: Διαστάσεις μοντέλου
0D. Μηδενικών διαστάσεων (σημείο)
1D. Μονοδιάστατο (γραμμής)
2D. Δισδιάστατο (επίπεδο)
3D. Τρισδιάστατο (κύβος)
Notes: The third step in model development is to determine whether a zero-, one-, two-,
or three-dimensional model is required and whether to nest the model. Three dimensional
models are ideal, but because such models require enormous computer time and memory, zero-, one-, and two-dimensional models are often used instead.
A zero-dimensional (0-D) model is a box model in which chemical and/or physical
transformations occur. Gases and particles may enter or leave the box from
any side. Since all material in the box is assumed to mix instantaneously, the concentration
of each gas and particle is uniform throughout the box. A standard
box model is fixed in space. A parcel model is a box model that moves through
space along the direction of the wind. Emission enters the box at different points
along the trajectory. Because a parcel model moves in a Lagrangian sense, it is also
called a Lagrangian trajectory model. Box models have been used to simulate photochemical
reactions that occur in smog chambers, fog production in a controlled
environment, and chemical and physical interactions between aerosol particles and
gases. Parcel models have been used to trace changes in an air parcel as it travels
from ocean to land and through the polar vortex.
A one-dimensional (1-D) model is a set of adjacent box models, stacked vertically
or horizontally. Vertical 1-D models may be used to study radiative transfer
with photochemistry, gas and aerosol vertical transport, aerosol optical properties,
aerosol sedimentation, or cloud convection. The main use of a horizontal 1-D
model is to test the 1-D advection diffusion equation. The disadvantage of a 1-D
model compared with a 2-D or 3-D model is that velocities in a 1-D model cannot
be predicted but must be estimated crudely. In addition, a 1-D model either
ignores gas, particle, and potential temperature fluxes through lateral (horizontal)
boundaries or roughly parameterizes them. Figure 11.11 shows results from a 1-D
photochemical-radiative model.
A two-dimensional (2-D) model is a set of 1-D models connected side by side.
2-D models can lie in the x–y, x–z, or y–z planes. Advantages of a 2-D over a
1-D model are that transport can be treated more realistically, and a larger spatial
region can be simulated in a 2-D model. 2-D models have been used, for example,
to simulate dynamics, transport, gas chemistry, and aerosol evolution (e.g.,
Garcia et al. 1992; Rahmes et al. 1998). A global 2-D model may stretch from
the South to the North Pole and vertically. South–north and vertical winds in such
a model are predicted or estimated from observations at each latitude and vertical
layer. Zonally averaged winds (west–east winds, averaged over all longitudes
for a given latitude and vertical layer) are needed in a 2-D global model. Such
winds are found prognostically or diagnostically. Prognostic winds are obtained,
for example, by writing an equation of motion for the average west–east scalar
velocity at each latitude and altitude. Diagnostic winds are obtained, for example,
by writing prognostic equations for south–north and vertical scalar velocities, then
extracting the average west–east scalar velocity from the continuity equation for
air.
A three-dimensional (3-D) model is a set of horizontal 2-D models layered on
top of one another. The advantage of a 3-D over a 2-D model is that dynamics and
transport can be treated more realistically in a 3-D model. The disadvantage of a
3-D model is that it requires significantly more computer time and memory than
does a 2-D model. Nonetheless, studies of urban air pollution are readily carried
out in 3-D, since simulation periods are generally only a few days. Computer-time
limitations are most apparent for global simulations that last months to years.
Because 3-D models represent dynamical and transport processes better than do
0-, 1-, and 2-D models, 3-D models should be used when computer time requirements
are not a hindrance.

## Slide 15: Χωρική & χρονική κλίμακα προσομοιώσεων
Notes: Urban air pollution, thunderstorms, and tornados are simulated over micro- to mesoscale domains. Acid deposition, regional climate
change, and hurricanes are simulated over meso- to synoptic-scale domains. Global climate change is simulated over a global domain. With respect to time, urban air
pollution and weather events are simulated over hours to weeks, acid deposition
events are simulated over days to months, and regional and global climate change
events are simulated over years to centuries.
Local scale: http://www.cerc.co.uk/environmental-software/ADMS-Urban-model.html

## Slide 16: 1. Μοντέλα τοπικής κλίμακας / ενδοαστικά
Περιγράφουν τις ατμοσφαιρικές διεργασίες σε επίπεδο δρόμου – πόλης, λαμβάνοντας υπόψη διαφορετικούς τύπους πηγών ρύπων (οδικές μεταφορές, βιομηχανία, οικιακές κλπ), την δομή του οριακού στρώματος, την τυρβώδη ροή, την ευστάθεια, το φαινόμενο των οδικών χαραδρών, καθώς και φωτοχημεία αέριων ρύπων.
Contour plot of London showing the annual average NO2 and O3 concentrations predicted by ADMS-Urban for 2008. NO2regions shown in yellow, orange or red are predicted to exceed the UK NAQS targets.

## Slide 17: 2. Περιοχικά/μέσης κλίμακας μοντέλα
Περιγράφουν τις ατμοσφαιρικές διεργασίες σε ευρύτερης περιοχής πόλης, χώρας ή ηπείρου λαμβάνοντας υπόψη διαφορετικούς τύπους πηγών ρύπων
(όλες τις μεταφορές, βιομηχανία, κεντρική θέρμανση κλπ), τύπους γης/εδαφοκάλυψης, συνοπτικά συστήματα, στρώμα ανάμιξης, τη φωτοχημεία αέριων ρύπων και σωματιδίων.

## Slide 18: 3. Παγκόσμιας κλίμακας μοντέλα
Χημικό μοντέλο φιλοξενείται εντός μετεωρολογικού, τα οποία επικοινωνούν και τα αποτελέσματα καλύπτουν όλον τον πλανήτη. Περιγράφονται οι ανθρωπογενείς και βιογενείς εκπομπές, ατμοσφαιρική χημεία, μεταφορά διάχυση, εναπόθεση κλπ
This portrait of global aerosols was produced by a GEOS-5 simulation at a 10-kilometer resolution. Dust (red) is lifted from the surface, sea salt (blue) swirls inside cyclones, smoke (green) rises from fires, and sulfate particles (white) stream from volcanoes and fossil fuel emissions. Image credit: William Putman, NASA/Goddard
Notes: http://www.ucsusa.org/global_warming/science_and_impacts/science/aerosols-and-global-warming-faq.html

## Slide 19: Τεχνική εστίασης (nesting)
Notes: A nested model is one that
contains two or more 3-D grid domains within it (where a grid domain is a 3-D
model, itself) within it, where all except one of the grid domains (the coarsestresolved)
receives outside boundary information from a domain with coarser
resolution. Grid domains that provide boundary conditions to finer-resolved domains in a
nested model are called parent domains. Domains that receive boundary conditions
from coarser (parent) domains are progeny domains. Since several domains can
be nested within each other (e.g., the Urban, R3, R2, R1, and global domains,
respectively, in Fig. 21.1), a domain can serve as both a parent and a progeny
domain. Each parent domain can also contain multiple progeny domains that are
independent of one another (e.g., the multiple R3 domains within the R2 domain in
Fig. 21.1).
Ideally, the coarsest-resolved domain in a nested model is the global domain,
which does not require boundary information, except at its base and top. In some
nested models, the coarsest domain is a limited-area domain, which needs lateral
boundary information. Such information can be obtained from interpolated
meteorological data or from stored global-model results. Variables passed at the
boundaries in a nested model are discussed in Section 21.1.11.
Nesting can be one-way or two-way.Aone-way nested model is a model in which
information is passed only from a parent to a progeny domain. A two-way nested
model is one in which information is passed in both directions. Most nested models
nest one way. One problem with two-way nesting is that it results in perturbations
to velocity, potential temperature, and other variables in the middle of the parent
domain that degrade conservation properties (e.g., conservation of mass, energy,
enstrophy, potential enstrophy, etc.) in the parent domains.

## Slide 20: Χωρική & χρονική κλίμακα προσομοιώσεων
Fig. 5. Spatial and temporal scales of air quality models based on Moussiopoulos et al. (2003).
Notes: https://www.esrl.noaa.gov/research/themes/aerosols/
Fig. 5. Spatial and temporal scales of air quality models based on Moussiopoulos et al. (2003). Resolution of CALINE4 and CAR traffic models is also indicated Urban scale and other larger scale models do not explicitly treat each building, but include the effect of them by using a corresponding roughness length. The model domain of an urban scale model is the size of an EU country or part of one (up to 500 km x 500 km). Urban scale models may be integrated for several days when using a nesting approach. They can resolve phenomena that have a characteristic time scale of more than 10 minutes and a characteristic horizontal scale of more than several hundreds of metres. The synoptic scale model domain covers the European-Atlantic region (5000 km x 5000 km) and the macro- scale models have a model domain that covers part of the globe (larger than 5000 x 5000 km 2 ).

## Slide 21: Χρονικό βήμα επίλυσης εξισώσεων
Εξαρτάται από
την επιθυμητή ακρίβεια,
τον διαθέσιμο υπολογιστικό χρόνο,
την διατήρηση της ευστάθειας του χρησιμοποιούμενου κώδικα.
Παραδείγματα:
For a 5-km × 5-km horizontal grid, a typical time step for hydrostatic dynamical calculations is 5 s.
For a 5◦ ×5◦ global grid, it is around 300 s.
For gas and aqueous chemistry, the time step is variable with some solution methods and fixed with others.
Notes: The continuity equation is numerically marched forward in time over a series of time steps. At
each step, the continuity equation is integrated by way of an operator‐splitting approach that
calculates the separate contribution of each major process (emission, advection, diffusion,
chemistry, and removal) to concentration change within each grid cell. The specific equations
that are solved individually in the operator‐splitting process are shown in order below:

## Slide 22: Χωρική & χρονική κλίμακα προσομοιώσεων
Fig. 1. MEGAPOLI schematic showing the main linkages between megacities, air quality and climate (Baklanov et al., 2010). In addition to the overall connections between megacities, air quality and climate, the figure shows the main feedbacks, ecosystem, health and weather impact pathways, and mitigation routes which are investigated. The relevant temporal and spatial scales are also included.

## Slide 23
Δομή Μαθήματος
Εισαγωγή
Χωρικές και χρονικές κλίμακες εφαρμογής μοντέλου ρύπανσης/ποιότητας ατμόσφαιρας
Κατηγοριοποίηση αριθμητικών μοντέλων
Χωρική και χρονική διακριτική ικανότητα εφαρμογής
Δεδομένα εισόδου σε μια αριθμητική προσομοίωση
Συνδυασμός με πειραματικά δεδομένα
Εφαρμογές μοντέλου – Έλεγχοι ευαισθησίας

## Slide 24: Τύποι μοντέλων / μέθοδοι υπολογισμών
Στατιστικά
Γκαουσιανά (Gaussian)
Τροχιάς (Lagrangian)
Κυψελίδας (Eulerian)
Δέκτη (Receptor)
Notes: Models can be generally divided into four categories, based on the methods used for the calculations: 1) statistical analysis models, 2) Gaussian models and 3) Lagrangian models. Most models, however, use an 4) Eulerian approach to calculate pollution transport. Some models may make use of more than one methodology and may fall into more than one category.

## Slide 25: Τύποι μοντέλων / μέθοδοι υπολογισμών
Στατιστικά:
Απλά μοντέλα διασποράς
Simplification is achieved primarily by ignoring the local, time-varying processes that affect short-term air pollutant concentrations (e.g. associated with variations in meteorology), and modelling instead the average (net) long-term patterns. Models thus comprise a series of formulae or statistical equations, which can be solved either arithmetically (e.g. using spreadsheet functions) or through the use of look-up tables and graphs.
GIS-based, για παράδειγμα παλινδρόμησης χρήσεων γης (LUR)
Εmpirically-derived regression equations linking land use (or more strictly land cover) to measured air pollutant concentrations at a set of monitoring sites. Other predictors are usually selected to represent traffic-related emissions (e.g. road length, traffic flows) in the surrounding area, and the effect of local topography (e.g. altitude).
Notes: Statistical models are based on relationships, usually originally founded in physical concepts, between observations and some other relevant parameters. There are a wide variety of statistical methods available including regression, neural networks, etc. that can be used. Since the relationships are based on observations, statistical models need to be established in each environment in which they are used. Statistical models simply require single-valued meteorological data extracted from a coupled meteorological model. They are not usually suitable for carrying out mitigation planning, as they do not causally relate emissions to concentrations.
Statistical models of air pollution have been developed primarily to provide a simpler and less data-demanding approach to estimating atmospheric concentrations, either for the purpose of air quality management (e.g. as screening models) or for exposure assessment in epidemiological studies. A range of approaches have been devised, so that statistical models take many different forms. Amongst these, two approaches are of particular utility in exposure assessment:
Εικονα: A NO2 LUR Model for Great Britain (GB) was constructed on the basis of monitored data representing annual mean concentrations of NO2 for the year 2001, derived from routine measurement sites from the national air quality network. Predictor variables used for modelling related to traffic, land use, topography and population. Data on the predictor variables were integrated in a GIS, and converted to 100x100m grids (raster). Using a “supervised stepwise regression” approach a best model was constructed and applied to the relevant predictor grids and a NO2 map for GB was created. This example is part of a publication (Vienneau et al., 2009) which compares LUR models between Great Britain and the Netherlands.

## Slide 26: Τύποι μοντέλων / μέθοδοι υπολογισμών
Gaussian:
dispersion model designed to determine air pollution concentrations at receptor locations downwind of highways located in relatively uncomplicated terrain. It incorporates (some of) transport, transformation, removal, thermodynamics, chemistry, heat transfer, aerosol loading, dense gas effects, surface and elevated sources, simple and complex terrain.
Steady or non- Steady-state.

## Slide 27: Τύποι μοντέλων / μέθοδοι υπολογισμών
Τροχιάς (Lagrangian):
pollutant particles in the atmosphere move along trajectories determined by the wind field, the buoyancy and the turbulence effects.
Notes: Puff models are an intersection between Gaussian and Lagrangian dispersion models. They hold the assumption that the concentration pattern can be well described with a Gaussian distribution; however, the centreline of a plume is not a straight downwind direction, but a Lagrangian trajectory.

## Slide 28
Μοντέλα κυψελίδας (Eulerian)
Notes: nested models have been developed that use a Lagrangian model near the source, but interpolate the variables on a grid to perform Eulerian dispersion and chemistry simulations for larger distances.

## Slide 29
Σύστημα κατακόρυφων συντεταγμένων
(σ-)υψομέτρου
(σ-)πίεσης
Ισεντροπικές
Notes: Jacobson: the equations of atmospheric dynamics can be solved either in fully compressible
form or after they are simplified with the hydrostatic, anelastic, or
Boussinesq approximation. In many cases, the equations are adapted to a vertical
coordinate other than the altitude coordinate. Such coordinates include the pressure,
sigma-pressure, sigma-altitude, and isentropic coordinates. The first three are
discussed in this chapter. A disadvantage of the altitude and pressure coordinates is
that both allow model layers to intersect ground topography. The sigma-pressure
and sigma-altitude coordinates are terrain-following and do not allow model layers
to intersect ground topography. A disadvantage of the pressure and sigma-pressure
coordinates is that both assume the atmosphere is in hydrostatic balance. Such an
assumption is reasonable for global and most mesoscale models but causes inaccuracy
for fine horizontal grid resolution, where the atmosphere is often nonhydrostatic.
For nonhydrostatic simulations, the altitude or sigma-altitude coordinate
can be used.

## Slide 30
Μοντέλα κυψελίδας (Eulerian): παραδείγματα αποτελεσμάτων

## Slide 31: Συζευγμένα ατμοσφαιρικά μοντέλα vs. Φωτοχημικά μοντέλα

## Slide 32: Μοντέλα Δέκτη (Receptor models)
Notes: Receptor models are mathematical or statistical procedures for identifying and quantifying the sources of air pollutants at a receptor location. Unlike photochemical and dispersion air quality models, receptor models do not use pollutant emissions, meteorological data and chemical transformation mechanisms to estimate the contribution of sources to receptor concentrations. Instead, receptor models use the chemical and physical characteristics of gases and particles measured at source and receptor to both identify the presence of and to quantify source contributions to receptor concentrations. These models are therefore a natural complement to other air quality models and are used as part of State Implementation Plans (SIPs) for identifying sources contributing to air quality problems.

## Slide 33: Μοντέλα Δέκτη (Receptor models)

## Slide 34: Μοντέλα Δέκτη (Receptor models)

## Slide 35
Δομή Μαθήματος
Εισαγωγή
Χωρικές και χρονικές κλίμακες εφαρμογής μοντέλου ρύπανσης/ποιότητας ατμόσφαιρας
Κατηγοριοποίηση αριθμητικών μοντέλων
Χωρική και χρονική διακριτική ικανότητα εφαρμογής
Δεδομένα εισόδου σε μια αριθμητική προσομοίωση
Συνδυασμός με πειραματικά δεδομένα
Εφαρμογές μοντέλου – Έλεγχοι ευαισθησίας

## Slide 36: Δεδομένα εισόδου στα μοντέλα

## Slide 37: Δεδομένα εισόδου στα μοντέλα

## Slide 38
Δεδομένα εισόδου στα μοντέλα

## Slide 39: Βάση εκπομπών (emission inventory)
Αρχεία με δεδομένα ρυθμών εκπομπής αέριων ρύπων, ανά έτος, ανά τύπο πηγής, ανά κυψελίδα.
SNAP source categories:
1 energy industry
2 residential combustion
3-4 industry
5 extraction/distribution FF
6 product use
7 road transport
8 other mobile sources
9 waste
10 agriculture

## Slide 40
Δεδομένα εισόδου στα μοντέλα

## Slide 41
Δεδομένα εισόδου στα μοντέλα

## Slide 42: Γεωγραφικά δεδομένα

## Slide 43
Δεδομένα εισόδου στα μοντέλα

## Slide 44
Δεδομένα εισόδου στα μοντέλα

## Slide 45
Δομή Μαθήματος
Εισαγωγή
Χωρικές και χρονικές κλίμακες εφαρμογής μοντέλου ρύπανσης/ποιότητας ατμόσφαιρας
Κατηγοριοποίηση αριθμητικών μοντέλων
Χωρική και χρονική διακριτική ικανότητα εφαρμογής
Δεδομένα εισόδου σε μια αριθμητική προσομοίωση
Συνδυασμός με πειραματικά δεδομένα
Εφαρμογές μοντέλου – Έλεγχοι ευαισθησίας

## Slide 46: Αφομοίωση δεδομένων (data assimilation)
Η ενσωμάτωση πειραματικών δεδομένων εντός αριθμητικού μοντέλου
Notes: http://www.allscale.eu/amdados: data assimilation

## Slide 47
Δομή Μαθήματος
Εισαγωγή
Χωρικές και χρονικές κλίμακες εφαρμογής μοντέλου ρύπανσης/ποιότητας ατμόσφαιρας
Κατηγοριοποίηση αριθμητικών μοντέλων
Χωρική και χρονική διακριτική ικανότητα εφαρμογής
Δεδομένα εισόδου σε μια αριθμητική προσομοίωση
Συνδυασμός με πειραματικά δεδομένα
Εφαρμογές μοντέλου – Έλεγχοι ευαισθησίας

## Slide 48: Εκτέλεση προσομοιώσεων
NOA - Thissio 37.97 N, 23.72 E, 105 m a.g.l.
Urban background site
Notes: After a model has been developed and input and ambient data have been gathered,
simulations can be run. When a simulation is first started, it usually does not run
to completion because programming bugs still exist in the program. Debugging
can take hours to weeks, depending on the number and severity of bugs and on
the debugging experience of the programmer. Nevertheless, bugs are usually ironed
out, and a baseline simulation can be performed.
Once a program has been debugged, it is ready for a baseline simulation. This
type of simulation includes all model processes and input data, and results from it
are often compared with ambient data. The primary purpose of model development
is to study a scientific or regulatory issue, and the baseline simulation should be
designed with such a study in mind. During a baseline simulation, model predictions
and statistical comparisons with data are often stored and/or printed out.
After the baseline simulation, sensitivity tests are often run to gauge the effect of
different assumptions on model performance. The results of such tests should be
compared with data and results from the baseline simulation.
For regional modeling, common sensitivity tests include testing changes in
boundary conditions, initial conditions, and emissions. One test is to set all inflow
gas and aerosol concentrations at horizontal boundaries equal to zero and compare
the results with those from the baseline case and with data. Another test is
to set all initial gas and aerosol concentrations to zero. A third test is to adjust
the emission inventory to estimate the effect of possible under- or overprediction
of emission on model results. On a global scale, sensitivity tests for emissions and
initial conditions can also be run.

## Slide 49: Εκτέλεση προσομοιώσεων